## Slide 1
3D Slicer Data Loading and Visualization Tutorial

## Slide 2: Tutorial dataset
Please download the following two datasets:
https://github.com/Slicer/SlicerDataLoadingAndVisualizationTutorial/raw/main/VisualizationTutorial_HeadScene.mrb

## Slide 3: Main user interface
Module panel
Data probe
3D view
Slice views

## Slide 4: Load sample MRI data

## Slide 5: Load sample MRI data

## Slide 6: Load sample MRI data
The axial, sagittal, and coronal views automatically show the loaded volume

## Slide 7: Adjust window/level
Switch to window/level mouse mode

## Slide 8: Adjust window/level
Adjust window/level (brightness/contrast) using the left mouse button on a slice view

## Slide 9: Switch back to view/transform mode

## Slide 10: Maximize view
Click on the maximize view button

## Slide 11: Slice view options
Position your mouse cursor over the pin icon to display the slice view toolbar

## Slide 12: Slice view options
Once the slice viewer toolbar is shown, click on the “>>”

## Slide 13: Show ruler

## Slide 14: Rotate to volume plane
Often, MRI volumes are not axis-aligned. To show the true axial view, click the ‘Rotate to volume plane’ button.
Note: This image will not be affected, but many DICOM MR images need to be aligned.

## Slide 15: Switch to conventional layout

## Slide 16: Link views
After linking views, if any setting is changed in a 2D view, all others follow.

## Slide 17: Show slices in 3D
Now the slice views are linked. If you click the ‘Toggle slice visibility in 3D view’ button, then all slices will show up.

## Slide 18: Show slices in 3D
All three anatomical slices are shown in the 3D view

## Slide 19: Navigating the 3D view
Use the left mouse button to rotate, and the right mouse button to zoom in and out

## Slide 20: Close the scene

## Slide 21: Part 2: 3D visualization of surface models of the brain

## Slide 22: Load tutorial scene
Drag and drop the file VisualizationTutorial_HeadScene.mrb into Slicer, then click OK

## Slide 23: Center view
Click on the small box icon to center the view, in 3D or in 2D

## Slide 24: Explore loaded data
You can use the module list, or the favorite module toolbar to switch to the Data module

## Slide 25: Explore loaded data
The Data module shows all the data in the scene.
The data items (“nodes”) can be shown/hidden, renamed, deleted, cloned, etc.
Hide the ‘skin’ model by clicking the eye icon.

## Slide 26: Foreground image
Images can be overlaid (“fused”) by setting the foreground image.
Select ‘T2 MRI’ as foreground
Adjust foreground opacity using the slider

## Slide 27: Create folder
Right-click the scene (or the empty area on the bottom), then choose ‘Create new folder’.

## Slide 28: Context menu actions
For list of “subject hierarchy” options for a certain node, right-click it in the list. Note that the options are different for each node type.
Right-click the just created folder ‘NewFolder’.

## Slide 29: Rename folder
Choose the Rename option and rename the volume to ‘White matter models’

## Slide 30: Select multiple nodes
Click ‘left cerebral white matter’, hold down Shift, and click ‘left cerebellar white matter’.
Note: You can use Control/Cmd button to select individually.

## Slide 31: Move nodes to folder
Drag&drop models into the folder

## Slide 32: Hide all nodes in folder
Click the eye icon of the ‘Models’ folder to hide all non-brain structures.

## Slide 33: Volume rendering
Click&drag volume to the 3D view.

## Slide 34: Display options
Right-click the eye icon to see display options. Choose ‘Volume rendering options…’. (It switches to the Volume Rendering module)

## Slide 35: Adjust volume rendering
Click on ‘Select a Preset’ and choose MR-Default.
Adjust the Shift slider to optimize visualization.

## Slide 36: Show models again
Turn off volume rendering using the eye icon.
Switch back to the Data module using the Modules history.

## Slide 37: Show models again
Show the folder again by clicking the closed eye icon in its row.

## Slide 38: Change skull model opacity
Right-click the eye icon of the skull model, select Opacity, and adjust the slicer to around 0.30

## Slide 39: Show axial slice in 3D
Hover the push-pin icon and then the eye icon to show a slice view in 3D view.

## Slide 40: Show coronal slice in 3D

## Slide 41: Model clipping
Right-click a model node in the data tree and choose ‘Edit properties…’ to go to the Models module. (It can be accessed from the toolbar or the module list as well)

## Slide 42: Model clipping
Select all brain models using Shift, then scroll down to the 3D Display section.

## Slide 43: Model clipping
Turn on Clipping.
Click Configure.

## Slide 44: Model clipping
Turn off Red Slice Clipping and turn on Green Slice Clipping.
The optic chiasm becomes visible in the 3D view

## Slide 45: 3D display options
Hide the coronal (green) plane. Position your cursor over the pin icon in the 3D view to display the 3D display options. Select the A (Anterior) view.

## Slide 46: Save the scene
Click the ‘Save data’ button.
Note: Also accessible from the File menu

## Slide 47: Save the scene
The Save Scene and Unsaved Data window lists all elements of the scene.
You can save as MRB bundle or as list of files.
Double-click the scene and rename it to myNewScene.mrb Click Save.

## Slide 48: Close the scene

## Slide 49: Load your recently saved scene
Load the new scene using the Recent data list.
(You can load the scene using drag&drop or Add data as well)

## Slide 50: Thanks for participating!